## Slide 1: Data-driven models for Alfvén eigenmode classification based on ECE diagnostics at DIII-D
Azarakhsh (Aza) Jalalvand
Data scientist at Ghent University - Belgium
Visiting postdoc at Plasma Control Group - Princeton University
Co-authors: A. Kaptanoglu, A. Garcia, A. Nelson, J. Abbate, M. Austin, G. Verdoolaege, S. Brunton, W. Heidbrink, E. Kolemen
Collaboration: DIII-D Team
Presented at the
APS-DPP meeting
November 2021
Notes: ELM detection with BES (Lakshya): CP11.00067, PP11.00160
Locating AE with ECE (Alan): CP11.00101, PP11.00154
AE spectrogram enhancement (Eric): JP11.00102
Autoencoder for BES compression (Prannav): JP11.00107
AE classification with CO2 (Alvin): PP11.00133
ELM detection with BES (Dave): PP11.00138
AE classification with RCN (Aza): TM10.00006
ML for plasma monitoring plasma – DOE project (Egemen): UM10.00003

## Slide 2: Alfvén eigenmode instabilities in DIII-D
Project:
  Machine Learning for Real-time Fusion Plasma Behavior Prediction and Manipulation (DE-SC0021275)
Data
  40 ECE diagnostics as inputs (ECEs provide spatial information)
Tasks
  Detect/classify Alfvén eigenmode (AE)
  Detect the location and shape of AE in plasma
  Predict and control AE

## Slide 3: Alfvén eigenmode dataset
919 shots of 2 seconds
5 AE modes (BAAE/LFM, BAE, EAE, RSAE, TAE)
Challenges
  Labels are not perfect
    Duration of events is not available
    Subject to the experts’ opinion (W.W. Heidbrink et al 2021 Nucl. Fusion 61 016029)
  Imbalanced data
  ECE is Noisy (Low SNR)
We did not do any preprocessing rather than mean-variance normalization on ECE signals

## Slide 4
Reservoir computing network (RCN)
  Recurrent neural network with Random connections
  Suitable for time-series data analysis
  Only Last layer is trained using linear regression.
Input to RCN: 40 ECE signals
Output: Probability of AE modes at each time step
Alfvén eigenmode classification using ECE

## Slide 5
True Positive Rate: %91
False Positive Rate: %7
Alfvén eigenmode classification using ECE

## Slide 6: Subsampling the ECE signals
  Hypotheses:
  Lower frequencies still contain enough information.
  The model’s memory covers missing data
  Other ideas?
  Subsampling the ECE signals has minor impact on the AE classification performance

## Slide 7: Conclusion
Promising performance in detecting AE modes With minimum feature engineering on ECE data
Possible future work
  Re-labeling the data using the current model’s output?
  Enriching the input features by including more diagnostics
  More advanced ML techniques
  Locating AE modes using ML and image processing techniques
Related presentations at APS-DPP21
  ML for monitoring plasma (overview of the DOE project): UM10.00003
  ELM detection using BES diagnostics: CP11.00067, PP11.00160
  Locating AE using ECE diagnostics: CP11.00101, PP11.00154
  AE spectrogram enhancement using image processing: JP11.00102
  Autoencoders for BES data compression: JP11.00107
  AE classification using interferometry data: PP11.00133
  ELM detection using BES diagnostics: PP11.00138

## Slide 8
Thank you!