## Slide 1
Stellarator optimization typically takes a two-stage approach:
  Stage 1: Optimize Physics Objectives To Obtain Boundary
  Stage 2: Minimize on Boundary to obtain Coils
Implementing coil optimization capabilities in DESC:
  Combine equilibrium + coil optimization code [cite Rogerio 1stage]
    Utilize DESC’s automatic differentiation
  Helical Coil Optimization: Limited options with current coil codes
Motivation
Helical Coil Design in DESC
Dario Panici1, Rory Conlin1, Todd Elder3, Rahul Gaur1, Daniel Dudt1, Tal Shpigel1,
Itay Gissis4, Nadav Snir4, Yasha Nikulshin4, Egemen Kolemen1,2
1 Princeton University, 2 Princeton Plasma Physics Laboratory , 3 Columbia University, 4 nT-Tao
DESC Stellarator Optimization Code
REGCOIL Algorithm
Results
Conclusions and Future Work
Coil Cutting Procedure
Visit
Our Website!
Acknowledgements
DESC1 is a 3D ideal MHD Stellarator Equilibrium and Optimization code2
Written in Python+JAX2 enables GPU + Automatic Differentiation capability
Extension underway to handle optimization of coils + surfaces + equilibria
REGCOIL3 algorithm being implemented as part of the coil capabilities
Using surface current distributions on a specified winding is an efficient approach to the coil-finding problem4,5
Then minimization of quadratic flux becomes a linear (in ) least-squares problem, after expanding in Fourier Series (I,G, and other terms are known)
However, can lead to poor solutions without regularization -> REGCOIL adds regularization to the problem based on the surface current
Helical coils found by specifying net toroidal current such that
Can calculate net toroidal or net poloidal current through a section of the surface as:
Each constant contour is a possible coil – can choose coils by picking contours starting from evenly spaced values in at
Assigning Coil Currents
To assign currents to the helical coils (in the absence of saddle coils), we can think of each coil has being responsible for the current up to halfway between its neighboring coils
To find the current this represents, we only need to consider the current entering the region from one side (due to K being divergence-free):
Current entering left region = current exiting right region
Only need to evaluate
Equal Current Algorithm
Equal current in all coils advantageous from engineering perspective
However, cannot naively pick equally spaced contours and set currents equal
Instead, minimize current difference w.r.t.
  Note: Sum of currents in coils must be equal to net toroidal current
Example helical coilset for QA Equilibrium on a circular toroidal winding surface
Demonstrates low normal field on surface
Can be extended to include external solenoid
REGCOIL algorithm implemented in Python+JAX inside of the DESC code suite
Helical coil cutting algorithms implemented, with capability to optimize chosen coil contours so that resulting coils have equal currents
Future work:
  Adding filamentary coil optimization capability to DESC
  Implement ability to handle saddle coils
  Using REGCOIL + AD to provide coil objectives for use in stellarator optimization
Quasisymmetry
Stability
Optimization Code (DESC)
Optimized Equilibrium
Minimize
Coil Optimization Code (DESC, REGCOIL, FOCUS)
Surface Current Density
Unit Normal to Winding Surface
Current Potential
: Surface Net Poloidal Current
: Surface Net Toroidal Current
0
b/c
Bot
Top
Current Potential On Winding Surface
Accounting For External Fields
The authors are grateful to Matt Landreman for help with understanding the REGCOIL algorithm
This work is supported by US DoE DE-AC02-09CH11466, DESC0022005, and Field Work Proposal No. 1019
References
[1] D. Panici, R. Conlin, D.W. Dudt, K. Unalmis, and E. Kolemen. The DESC stellarator code suite. Part 1. Quick and accurate equilibria computations. JPP, 89(3):955890303, Jun. 2023.
[2] J. Bradbury et al, JAX: composable transformations of Python+NumPy programs. 2018.
[3] M. Landreman. An improved current potential method for fast computation of stellarator coil shapes. Nuclear Fusion, 57(4):046003, April 2017.
[4] P. Merkel. Solution of stellarator boundary value problems with external currents. Nuclear Fusion, 27(5):867–871, May 1987.
Total net poloidal current outside plasma determined by equilibrium field
External coils (TF, PF, Planar, etc) may be present outside of winding surface - must account for this!
Fig: Equilibrium (red-blue) with representative winding surface (grey) with helical coils (black) inside an external planar coil set (orange)
0.24
0.18
0.12
0.06
0.00
-0.06
-0.12
-0.18
-0.24
-0.30
0.60
0.45
0.30
0.15
0.00
-0.15
-0.30
-0.45
-0.60
0.040
0.032
0.024
0.016
0.008
0.000
-0.008
-0.016
-0.024
-0.032
Current per Coil | 73.35 KA
Number of Coils | 12
Max Bnormal on Plasma Surface | 1.1e-3 T