## Slide 1: Near-Axis Constrained Equilibria with the DESC code
Dario Panici, Daniel Dudt, Rory Conlin, Eduardo Rodriguez, Egemen Kolemen

## Slide 2: Near-Axis-Expansion Constrained Equilibria in DESC
Global equilibria solutions with near-axis behavior constrained to match the NAE to O()
Enables the connection between global MHD equilibria solutions and the existing insight on optimized stellarators
NAE-constrained equilibrium iota matches NAE near axis
NAE-constrained equilibrium maintains better QS near axis
Notes: QSC Equilibrium from Eduardo Rodriguez
NAE evaluated at r =0.1

## Slide 3: Ideal MHD Equilibrium Inverse Equilibrium Problem
Cast problem as solving for the locations of the flux surfaces
Yields 2nd order PDE in (𝝆,𝜽,𝞯)
Notes: Physically, the force balance tells us…
Simple 1D example is an infinitely long, rotationally symmetric cylindrical plasma with current running axially, called a Z-pinch
Additionally, we can see that by taking dot products with B and J, that both these fields lie on surfaces of constant pressure CLICK
these are called ‘flux surfaces’, and are surfaces upon which the B field is everywhere tangential. Shown here are the flux surfaces for this 1D example

## Slide 4: Stellarator Equilibrium - DESC
(Dudt and Kolemen 2020)
3D Ideal MHD Equilibrium Code
Assumes Nested Flux Surfaces
Inverse Equilibrium Problem
Minimizes Force Error Directly
Pseudospectral Code
Notes: Now let me introduce the DESC code
DESC solves the same problem as VMEC does, but in a different way
While VMEC minimizes energy, DESC minimizes the force error directly
Further, DESC is a pseudospectral code with a spectral basis for both the angular dependence AND the radial dependence
this allows analytic radial derivatives, not finite differences like VMEC must use
Additionally, by casting our problem as finding the roots to the force error residual on the collocation grid, we can use Newton methods

## Slide 5: DESC - Fourier-Zernike Spectral Basis
Zernike Polynomials in plane
Zernike Polynomials
Toroidal Fourier Series
Radial Polynomial is of degree l-2s, and l=m,m+2,…, L

## Slide 6: DESC Allows Flexible Constraints when Defining Equilibrium Problem - Fixed 𝝆=1 Boundary
Fixed-Boundary 𝝆=1 Constraint
Zernike Polynomials

## Slide 7: Near-Axis Expansion (NAE) Constraints in DESC (with E. Rodriguez)
Idea is to constrain the global equilibrium to have NAE behavior as 𝝆→𝟢
  only use information from NAE where it is most valid
  Avoid singular behavior present when evaluating at large r
Map NAE coefficients to Fourier-Zernike modes of DESC to fix O(𝝆0) (axis), O(𝝆1), O(𝝆2) behavior
pyQSC equilibrium evaluated at r =0.1

## Slide 8: O(𝝆0) (axis) Constraint in DESC
NAE axis in pyQSC given as Fourier series in cylindrical toroidal angle 𝝓:
Constraint in DESC representation is simple: Evaluate DESC R(𝝆,𝜃,𝝓), Z(𝝆,𝜃,𝝓) at 𝝆=0 and match terms:
NAE Axis Coefficients
DESC Fourier-Zernike Coefficients
Notes: obviously, is an underconstrained system, is initial guess dependent (show same axis and 2 different equilibria?)
But opens opportunity to keep the same axis optimized in pyQSC
Further, can constrain near-axis behavior to match the NAE as well

## Slide 9: O(𝝆1) NAE Constraint in DESC
NAE Coefficients
DESC Fourier-Zernike Coefficients
- After a short geometric derivation, one can derive (up to O(𝝆)) the R,Z position of a point on a flux surface from the NAE in terms of the cylindrical angle
where
- And the coefficients are functions of the NAE X,Y coefficients and the Frenet-Serret basis vectors
- Then, equating the O(𝝆) coefficients in the DESC Fourier-Zernike basis with the above expressions yields:
(Identical expressions for Z as well)
Notes: boozer poloidal angle - mention

## Slide 10: Verification of DESC Equilibrium Quantities Against the NAE
Magnetic Axis and Near-Axis Flux Surfaces
On-axis Rotational Transform
Near-Axis Confinement
(fB for QS, for QI)
On-axis Poloidal Angle ()
On-axis Magnetic Field Magnitude
Will show 3 examples: QA, QH, and a QI NAE-constrained equilibrium

## Slide 11: QA O(𝝆1) NAE-constrained Equilibrium
pyQSC based on Precise QA from (Landreman and Paul 2022)

## Slide 12: QH O(𝝆1) NAE-constrained Equilibrium
pyQSC based on Precise QH from (Landreman and Paul 2022)

## Slide 13: QI O(𝝆1) NAE-constrained Equilibrium
pyQIC based on QI from section 8.2 of (Plunk, Landreman and Helander 2019)

## Slide 14: Example Python Code for NAE-Constrained Equilibria in DESC – Simple!
# imports
from qsc import Qsc
from desc.objectives import get_NAE_constraints
from desc.equilibrium import Equilibrium
# fit initial DESC equilibrium from desired qsc solution
qsc = Qsc.from_paper('precise QA',nphi=99)
desc_eq = Equilibrium.from_near_axis(qsc,r=0.35,L=9,M=9,N=10)
# get constraints on axis and O(r) coefficients
# to pass to eq.solve using utility function
cs = get_NAE_constraints(desc_eq, qsc, order=1)
# solve NAE-constrained equilibrium
desc_eq.solve(objective=”force”,constraints=cs);
Tutorial on DESC documentation website: desc-docs.readthedocs.io

## Slide 15: QA O(𝝆2) NAE-constrained Equilibrium

## Slide 16: Fitting NAE Behavior with Toroidal Fourier Series – O()
O() Coefficient
QA NAE behavior simplest to describe
QI NAE behavior very difficult to describe with cylindrical angle!

## Slide 17: Fitting NAE Behavior with Toroidal Fourier Series – O()
O() Coefficient
O() Coefficient
O() NAE behavior much easier to describe with cylindrical angle than O()
O() – constrained equilibria may require very high Ntor to capture behavior accurately
Generalized toroidal angle may help condense spectrum

## Slide 18: (REG)Coil Optimization In DESC

## Slide 19: REGCOIL Algorithm
Using surface current distributions on a specified winding is an efficient approach to the coil-finding problem4,5
Then minimization of quadratic flux becomes a linear (in ) least-squares problem, after expanding in Fourier Series (I,G, and other terms are known)
However, can lead to poor solutions without regularization -> REGCOIL adds regularization to the problem
Surface Current Density
Unit Normal to Winding Surface
Current Potential
: Surface Net Poloidal Current
: Surface Net Toroidal Current

## Slide 20: Helical Coilset in DESC
REGCOIL Algorithm implemented in DESC to find surface currents
Helical coil-cutting capabilities also implemented to discretize into helical coils
Helical Coilset

## Slide 21: Example Python Code to create Helical Coilset
# load equilibrium, this case is a simple vacuum rotating ellipse
eqname = "./tests/inputs/ellNFP4_init_smallish.h5"
eq = load(eqname)
# get the surface current which minimizes Bn with REGCOIL algorithm
(surface_current_field, _, _, _, _,) = run_regcoil(
eqname=eq,
# resolutions of plasma surface grid upon which Bn is minimized
eval_grid_M=20,eval_grid_N=20,
# resolutions of source grid for calculating Bn
source_grid_M=40, source_grid_N=80,
alpha=1e-15, # regularization parameter
# ratio of I/G, 0 for modular, integer for helical coils
helicity_ratio=-1)
# discretize into helical coils using utility function
numCoils = 15 # we want 15 helical coils
coilset2 = find_helical_coils(surface_current_field, eqname, desirednumcoils=numCoils)
Notes: Default winding surface is being used here which is an axisymmetric torus

## Slide 22: Example Python Code to create Modular Coilset
# load equilibrium, this case is a simple vacuum rotating ellipse
eqname = "rotating_ellipse_5_aspect_ratio.h5"
eq = load(eqname)
winding_surf= load(“rotating_ellipse_wind_surf.h5”)
# get the surface current which minimizes Bn with REGCOIL alg
(surface_current_field, _, _, _, _,) = run_regcoil(
eqname=eq, basis_M=16, basis_N=16,
# resolutions of plasma surface grid upon which Bn is minimized
eval_grid_M=60,eval_grid_N=60,
# resolutions of source grid for calculating Bn
source_grid_M=100, source_grid_N=100,
alpha=1e-16, # regularization parameter
# ratio of I/G, 0 for modular, integer for helical coils
helicity_ratio=0, winding_surf = winding_surf)
# discretize into modular coils using utility function
numCoils = 60 # we want 60 modular coils, (15 per field period)
coilset2 = find_modular_coils(surface_current_field,
eqname, desirednumcoils=numCoils)

## Slide 23: DESC Offers Unique Flexibility in Constraints that Open New Possibilities
NAE Constrained Equilibrium Solve
  Can offer connection between rich NAE+QS theory and global solutions
  Allow global solutions to be found matching NAE axes that otherwise could not be found traditionally
  Verified against pyQSC and pyQIC for O(rho) constraints
  Ongoing verification of 2nd order constraints
    Can allow geometrically constraining on-axis Mercier stability, for example
  Can be used with DESC constrained optimization
  Available to use now in main DESC code
DESC Coil Optimization
  REGCOIL algorithm implemented in Python
  Modular and Helical Coil-cutting algorithms implemented
  Written in JAX, so can be used with optimization, combined with other objectives
    Single-stage optimization?
  Will be available soon in main DESC code

## Slide 24: Backup

## Slide 25: O(𝝆0) (axis) Constraint in DESC - Example Solve

## Slide 26: O(𝝆0) (axis) Constraint in DESC - Under-constrained Problem, Finds Closest Equilibrium
Different Initial Guess
Notes: want to emphasize the non-uniqueness of the constraint here, this goes as well for the NAE constrain I will show next

## Slide 27: Physical Insights Yield Constraints on XS or near Axis
Axis + Near-Axis Behavior
Near-Axis Expansion (NAE) yields what asymptotic behavior of equilibrium should be near the axis, and what the axis shape should be
Poincare Section
Desire to avoid magnetic islands, and decoupling poloidal and toroidal resolution
Notes: We ideally want to fix our desirable qualities stemming from other theory like NAE, which tells us information about an axis and the equilibrium shape asymptotically near the axis, which we know to be in equiibrium, or we can optimize for QS or QI.
Or we want our surfaces to be island-free,

## Slide 28: Closer look at flux surfaces near axis for Precise QA

## Slide 29: Closer look at flux surfaces near axis for difficult NAE (from E. Rodriguez)
rc = [1, 0.426, 0.044, -6.3646383583351e-11, 2.851584586653665e-05, 3.892992983405039e-08]
zs = [0.0, 0.4110168175146285, 0.04335427796015756, 6.530936323433338e-05, 1.3623898672936873e-05, 1.1620514629503932e-05]
etabar=1.64209358
B2c = 0.11293987662545873
B0=1
nfp = 4
qsc = Qsc(rc=rc, zs=zs, B0=B0, nfp=nfp, I2=0, B2c = B2c, etabar=etabar, order = "r1", nphi = 201)
desc_eq= Equilibrium.from_near_axis(qsc,r= r,L=9,M=9,N=N,ntheta=ntheta)

## Slide 30: Closer look at LCFS for difficult NAE (from E. Rodriguez)
rc = [1, 0.426, 0.044, -6.3646383583351e-11, 2.851584586653665e-05, 3.892992983405039e-08]
zs = [0.0, 0.4110168175146285, 0.04335427796015756, 6.530936323433338e-05, 1.3623898672936873e-05, 1.1620514629503932e-05]
etabar=1.64209358
B2c = 0.11293987662545873
B0=1
nfp = 4
qsc = Qsc(rc=rc, zs=zs, B0=B0, nfp=nfp, I2=0, B2c = B2c, etabar=etabar, order = "r1", nphi = 201)
desc_eq= Equilibrium.from_near_axis(qsc,r= r,L=9,M=9,N=N,ntheta=ntheta)

## Slide 31: O(𝝆0) (axis) Constraint in DESC - Under-constrained Problem
Different Initial Guess

## Slide 32: Near-Axis Expansion
Quantities are expanded in form
Inputs for solutions
  Axis Shape (R(phi), Z(phi))
  Measure of magnetic field variation
  Deviation from stellarator symmetry at
    Taken as 0 for most cases
  Current Density on axis
  Pressure near axis
  magnetic field poloidal variation
Outputs:
Flux surface shapes in neighborhood of axis
rotational transform on-axis
magnetic field variation on-axis
(Landreman 2022)
(Jorge 2022)
Notes: Note that the QS is not guaranteed thru O(rho^2) (Garren-boozer), instead it is guaranted thru O(rho) away from axis
To get QS solutions, how the qsc code does it is that it optimizes the inputs B_2c etc to find the minimal B_20, since B_20 should be 0 in a perfectly QS device

## Slide 33: DESC Allows Flexible Constraints when Defining Equilibrium Problem - Fixed 𝝆=1 Boundary
Fixed-Boundary 𝝆=1 Constraint
Zernike Polynomials
Notes: (M+1)(2M+1)*2 ~ 4M^2

## Slide 34: DESC Algorithm
Inputs
Scale Boundary as Initial Guess for Surface Geometry
Fourier Series
Compute B and J from
Compute on collocation grid
Initialization
Main Algorithm
Repeat until converged
Increase Collocation Grid and/or Spectral Resolution
Repeat until Desired Resolution
, use Newton Method to find
Notes: Show a pic for the Initial guess and boundary
like a simple circle, then you can show the fourier coeffs of the boundary
And profiles for iota and pressure
how does one choose these?
based off of desired boundary shape (this is fixed boundary), and desired iota, and the pressure can be chosen to match experimental-like profiles, and psi_a only scales the strength of the B field, not the geometry (I think)
And the timestepping is really a second order Richardson scheme
should change that
Point out differences btwn VMEC and DESC